## Slide 1: Designing a PID controller using analog input and analog output signals using digital and analog components for laboratory use
Pranabendra Prasad Chandra
001610801122

## Slide 2: Top View of the Controller
SCOPE
SCOPE
SET
POINT
TO PLANT
FEEDBACK
CONTROLLER

## Slide 3: Block diagram of digital PID in hardware

## Slide 4: Simulation Result

## Slide 5: Block diagram of digital PID in hardware

## Slide 6: Block diagram of digital PID in hardware
Signal Generator – 10 Vp-p (max)
Sine Square Triangle

## Slide 7: Block diagram of digital PID in hardware
V- : 10 Vp-p
V+ : 10 Vp-p
e(t) : 0-5V
Op amp : OP07
2.5V Zener : 1N5222B

## Slide 8: Block diagram of digital PID in hardware
Microcontroller : Arduino Mega
Voltage Input : 5V Regulated DC
Sampling Frequency : 5000 Hz (max 9 kHz)
PWM Switching Frequency : 5000 Hz
20x4 LCD
Keypad
5V PWM

## Slide 9: Block diagram of digital PID in hardware
Low Pass Filter
Cut-off frequency should be less than the switching frequency
But, cut-off frequency should be high enough to pass the setpoint
Here, cut-off frequency is 160 Hz (tuneable)

## Slide 10: Block diagram of digital PID in hardware

## Slide 11: Power Lines

## Slide 12: Protection
Risk
Chance of pressing multiple buttons together
Shorting the output
Putting input signal in output port
Overvoltage in mains
Overcurrent from mains
Remedy
Latching the first button pressed
Current limiting resistor
Buffer
P.T. + Relay
C.T. + Relay

## Slide 14: References
Secrets of Arduino PWM (Link)
Basic Calculation of an Inverting Buck-Boost Power Stage – Texas Instruments (Link)